## Slide 1: FreeRTOS with CubeMX
Technically Oriented Microcontroller Application Services
Bruno Montanari – bruno.montanari@st.com

## Slide 2: Agenda
2
Cube and Keil system check
 What is CubeMX?
Creation and tuning of a simple project using SWO from SWD intreface
FreeRTOS Basics
FreeRTOS hands on for several features
task/priorities/timers/mutex/semaphores (not in this order) 

## Slide 3: Cube and Keil check

## Slide 4: STM32Cube Install
STM32CubeMX tool
  http://www.st.com/stm32cube
The STM32CubeMX tool needs Java
  Please check whether you have latest Java installed on your PC, for sure 32-bit and 64-bit version
You can either download STM32CubeF4 packages directly from STM32CubeMX or download them offline using the below links and install as local (“From loc…” button)
  STM32CubeF4
12

## Slide 5: STM32Cube configuration 1/3
In case you download packages from web, you need to define place where they will be stored (repository)
MENU>Help>Updater Settings…
You will see current repository folder location
  Default is C:/User/Acc_name/STM32Cube/Repository/
  NOTE: In case your repository path contains diacritics, STM32CubeMX may fail to recognize them correctly. If this happens, change your repository path to contain raw Latin only (ex: C:/Repository)
You can either download STM32 packages manually and put them
into this folder or STM32CubeMX can do it for you if configured correctly

## Slide 6: STM32Cube configuration 2/3
The comparison of the STM32CubeMX repository settings and folder structure
In case you want STM32CubeMX to download these files automatically
  MENU>Help>Install New Libraries
  Select required libraries
  Force download with button “Install Now”
STM32CubeMX can download for you repository packages automatically

## Slide 7: STM32Cube configuration 3/3
The comparison of the STM32CubeMX repository settings and folder structure
In case you want to install files manually
  MENU>Help>Install New Libraries
Click “From Local…” button
Browse to select file
15

## Slide 8
For code generation STM32CubeMX uses package from the Repository folder
Currently, STM32CubeMX can generate code for the following toolchains
  Keil (free for F0/L0 families)
  IAR
  Atollic (free Lite version available)
  System Workbench (SW4STM32 by AC6, free)
For debugging purposes, it is necessary to have ST-Link drivers installed.
Drivers are a part of ST-Link Utility package that can be found here
  STSW-LINK004 ST-link Utility
To install drivers you will need Admin rights on your PC
STM32CubeMX install

## Slide 9: Checkpoint #1
Help->About
Help->Install New Libraries

## Slide 10: Checkpoint #2 – Keil verification
9
Open Keil v5

## Slide 11: What is CubeMX?

## Slide 12: STM32CubeMX applixation
STM32CubeMx do allow to configure peripherals using GUI, generate project framework and peripheral initialization code.
STM32CubeMx do not allow to create algorithms using GUI and generate algorithms code yet – there is still some space for programmers left ;-)
5

## Slide 13: What is CubeMX?
6
Pinout Wizard
Clock Tree Wizard
Peripherals & Middleware Wizard
Power Consumption Wizard
STM32CubeMX
Generates Initialization C Code based on user choices !

## Slide 14: What is CubeMX?
Middleware
ST
STemWin
STM32_Audio
STM32_USB_Device_Library
STM32_USB_Host_Library
Third Party
FatFS
FreeRTOS
LibJPEG
LwIP
PolarSSL
Advanced set of libraries
Third Party libraries
Developed/Owned by ST
Cube F4 HAL package
Documents
Drivers
Middleware
Projects
Utilities

## Slide 15: Using SWO to print information from STM32

## Slide 16: Using SWO
On some stm32 is periphery called ITM, not mix with ETM(real trace)
This periphery can be used to internal send data from MCU over SWO pin
Is possible to redirect the printf into this periphery
And also some IDEs can display this information during debug
It is similar to USART but we don’t need any additional wires and PC terminal
Video: Link

## Slide 17: Using SWO
Create a new Cube project for our eval kit

## Slide 18: Using SWO for printf
We need only blank project with clock initialization
  We set the and configure the core to maximum speed and SWD with SWO and the SYS interface to handle the Trace Asynchronous

## Slide 19: Using SWO for printf
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code

## Slide 20: Using SWO for printf in KEIL
We need to include the stdio.h library to make printf working
And define __FILE structure
fputc function must be defined to send byte over ITM
/* USER CODE BEGIN Includes */
#include <stdio.h>
/* USER CODE END Includes */
/* USER CODE BEGIN PFP */
struct __FILE { int handle; /* Add whatever is needed */ };
/* USER CODE END PFP */
/* USER CODE BEGIN 4 */
/*send text over SWV*/
int fputc(int ch, FILE *f) {
ITM_SendChar(ch);//send method for SWV
return(ch);
}
/* USER CODE END 4 */

## Slide 21: Using SWO for printf in KEIL
If the MCU run on very high frequency and you not see print f output you may try put into ITM send delay loop
/* USER CODE BEGIN 4 */
/*send text over SWV*/
int fputc(int ch, FILE *f) {
uint32_t i=0;
for(i=0;i<0xFFFF;i++);//waiting method, lower value will stop the SWV
ITM_SendChar(ch);//send method for SWV
return(ch);
}
/* USER CODE END 4 */

## Slide 22: Using SWO for printf in KEIL
In KEIL
Open target options (ALT+F7)
Set ST-Link debugger
Button Settings
Set SW(D) in Debug TAB
Got to Trace TAB
1. Target options
2. Select DEBUG tab
3. Set ST-Link
4. Open Settings
5. Set SW(D)
6. Go to Trace tab

## Slide 23: Using SWO for printf in KEIL
Check Trace Enable
Set core clock (84MHz must be same as in CubeMX clock tree)
ITM Stimulus Port 0 must be checked
Button OK
4. Open Settings
1. Trace Enable
2. Set Core clock
3. Check ITM Port 0
4. Button OK

## Slide 24: Using SWO for printf in KEIL
Testing loop printf in main
Compile and debug project
Open Debug (printf) Viewer
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
printf("test text\n");
HAL_Delay(1000);
}
/* USER CODE END 3 */

## Slide 25: Using SWO for printf in IAR
Here is configuration more easier
Open project options
General Options
TAB library and configuration
Select stdout/stderr via SWO
Button OK
2. Library configuration
1. General options
3. Set Via SWO

## Slide 26: Using SWO for printf in IAR
Add testing printf into loop
Compile project and go to debug
Open SWO
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
printf("test text\n");
HAL_Delay(1000);
}
/* USER CODE END 3 */
Open SWO options

## Slide 27: Using SWO for printf in IAR
Override project default if clocks are different from core (168MHz in out case)
Check autodetect SWO clock if possible
Enable ITM Port 0 to terminal
Button OK
Override clock and set correct value (168MHz)
Check autodetect
Enable ITM Port 0
Button OK

## Slide 28: Using SWO for printf in IAR
Menu View -> Terminal I/O
Run program

## Slide 29: FreeRTOS

## Slide 30: FreeRTOS About FreeRTOS
Market leading RTOS by Real Time Engineers Ltd.
Professionally developed with strict quality management
Commercial versions available: OpenRTOS and SafeRTOS
Documentation available on www.freertos.org
Free support through forum (moderated by RTOS original author Richard Barry)

## Slide 31: FreeRTOS Main features
Preemptive or cooperative real-time kernel
Scalable RTOS with tiny footprint (less than 10KB ROM)
Includes a tickless mode for low power applications
Synchronization and inter-task communications using
  message queues
  binary and counting semaphores
  mutexes
  group events (flags)
Software timers for tasks scheduling
Execution trace functionality
CMSIS-RTOS API port

## Slide 32: FreeRTOS APIs overview (1/2)
API category
FreeRTOS
API
Description
Task
creation
xTaskCreate
Creates a new
task
vTaskDelete
Deletes a task
Task control
vTaskDelay
Task delay
vTaskPrioritySet
Set
s task priority
vTaskSuspend
Suspends
a task
vTaskResume
Resumes
a task
Kernel control
vTaskStartScheduler
Starts
kernel scheduler
vTaskSuspendAll
Suspends all tasks
xTaskResumeAll
Resumes all
tasks
taskYIELD
Forces
a context switch
taskENTER_CRITICAL
Enter
a critical section (stops
context switching)
taskEXIT_CRITICAL
Exits
from a critical section

## Slide 33: FreeRTOS APIs overview (2/2)
API
category
FreeRTOS
API
Description
Message
queues
xQueueCreate
Creates
a queue
xQueueSend
Sends
data to queue
xQueueReceive
Receive
data from the queue
Semaphores
xSemaphoreCreateBinary
Creates
a binary semaphore
xSemaphoreCreateCounting
Creates
a counting semaphore
xSemaphoreCreateMutex
Creates a mutex semaphore
xSemaphoreTake
Semaphore
take
xSemaphoreGive
Semaphore give
Timers
xTimerCreate
Creates a timer
xTimerStart
Starts
a timer
xTimerStop
Stops a timer

## Slide 34: FreeRTOS CMSIS-RTOS FreeRTOS implementation
Implementation in file cmsis-os.c (found in folder: “\Middlewares\Third_Party\FreeRTOS\Source\CMSIS_RTOS”)
The following table lists examples of the CMSIS-RTOS APIs and the FreeRTOS APIs used to implement them
API category | CMSIS_RTOS API | FreeRTOS API
Kernel control | osKernelStart | vTaskStartScheduler
Thread management | osThreadCreate | xTaskCreate
Semaphore | osSemaphoreCreate | vSemaphoreCreateBinary xSemaphoreCreateCounting
Mutex | osMutexWait | xSemaphoreTake
Message queue | osMessagePut | xQueueSend xQueueSendFromISR
Timer | osTimerCreate | xTimerCreate
Note: CMSIS-RTOS implements same model as FreeRTOS for task states

## Slide 35: FreeRTOS CMSIS-RTOS API
CMSIS-RTOS API is a generic RTOS interface for Cortex-M processor based devices
Middleware components using the CMSIS-RTOS API are RTOS agnostic, this allows an easy linking to any third-party RTOS
The CMSIS-RTOS API defines a minimum feature set including
  Thread Management
  Kernel control
  Semaphore management
  Message queue and mail queue
  Memory management
  …
For detailed documentation regarding CMSIS-RTOS refer to: http://www.keil.com/pack/doc/CMSIS/RTOS/html/index.html

## Slide 36: FreeRTOS Configuration options
Configuration options are declared in file FreeRTOSConfig.h
Important configuration options are:
Config option | Description
configUSE_PREEMPTION | Enables Preemption
configCPU_CLOCK_HZ | CPU clock frequency in hertz
configTICK_RATE_HZ | Tick rate in hertz
configMAX_PRIORITIES | Maximum task priority
configTOTAL_HEAP_SIZE | Total heap size for dynamic allocation
configLIBRARY_LOWEST_INTERRUPT_PRIORITY | Lowest interrupt priority (0xF when using 4 cortex preemption bits)
configLIBRARY_MAX_SYSCALL_INTERRUPT_PRIORITY | Highest thread safe interrupt priority (higher priorities are lower numeric value)

## Slide 37: FreeRTOS Tickless idle mode operation
Kernel can stop system tick interrupt and place MCU in low power mode, on exit from this mode systick counter is updated
Enabled when setting configUSE_TICKLESS_IDLE as 1
The kernel will call a macro portSUPPRESS_TICKS_AND_SLEEP() when the Idle task is the only task able to run (and no other task is scheduled to exit from blocked state after n ticks)
  n value is defined in FreeRTOSconf.h file
FreeRTOS implementation of portSUPRESS_TICKS_AND_SLEEP for cortexM3/M4 enters MCU in sleep low power mode
Wakeup from sleep mode can be from a system interrupt/event

## Slide 38: FreeRTOS in CubeMX
Use CubeMX project from printf example
In Pinout TAB select in MiddleWares FreeRTOS
In Configuration TAB is now possible to configure FreeRTOS Parameters

## Slide 39: CubeMX FreeRTOS Configuration
FreeRTOS configuration supported by CubeMX
Config parameters
  Set kernel
  Mem setup
Include parameters
  Include some additional functions, not necessary for FreeRTOS run
Tasks and Queues
  We can easily create task or queue by CubeMX
Timers and semaphores
  CubeMX create semaphore and timer for us

## Slide 40: Kernel settings
Use preemption
  If enabled use pre-emptive scheduling
  If disabled use co-operative scheduling
Task1
Priority level
High priority
Low priority
time
Create Task2
Task1 suspend
Task2
Task1
Priority level
High priority
Low priority
time
Create Task2
Task2 suspend
Task1
Task2

## Slide 41: FreeRTOS Memory allocations types

## Slide 42: FreeRTOS Dynamic memory management
FreeRTOS have own heap which is use for components
  Tasks
  Queues
  Semaphores
  Mutexes
  Dynamic memory allocation
Is possible to select type of memory allocation
Total heap size for FreeRTOS
How is memory allocated and dealocated

## Slide 43: FreeRTOS Dynamic memory management
Heap
Heap_1.c
  Simplest allocation method (deterministic), but does not allow freeing of allocated memory => could be interesting when no memory freeing is necessary
Heap
Allocated block 2
Allocated block 1
Allocated block 3
pvPortMalloc
pvPortMalloc
pvPortMalloc
vPortFree
vPortFree
vPortFree
Is not possible to return memory to heap

## Slide 44: FreeRTOS Dynamic memory management
Heap
Heap_2.c
  Implements a best fit algorithm for allocation
  Allows memory free operation but does not combine adjacent free blocks => risk of fragmentation
Heap
Allocated block 2
Allocated block 1
Allocated block 3
pvPortMalloc
pvPortMalloc
pvPortMalloc
vPortFree
vPortFree
Heap 1
Heap 2
Allocated block 1
Heap 3
vPortFree
Heap 1
Heap 2
Heap 4
Heap 3
Free blocks are not combined together

## Slide 45: FreeRTOS Dynamic memory management
Heap
Heap_3.c
  Implements a simple wrapper for the standard C library malloc() and free(), the wrapper makes these functions thread safe, but makes code increase and not deterministic
Heap
Allocated block 2
Allocated block 1
Allocated block 3
malloc
malloc
malloc
free
free
Heap 1
Heap 2
Allocated block 1
Heap 3
free
Heap 1
Heap 2
Heap 4
Heap 3
Use C functions for allocation (linker must be modified)

## Slide 46: FreeRTOS Dynamic memory management
Heap
Heap_4.c
  First fit algorithm and able to combine adjacent free memory blocks into a single block => this model is used in STM32Cube examples
Heap
Allocated block 2
Allocated block 1
Allocated block 3
pvPortMalloc
pvPortMalloc
pvPortMalloc
vPortFree
vPortFree
vPortFree
Heap 1
Heap 2
Allocated block 1
vPortFree
Heap
combine together free memory

## Slide 47: Memory allocation
Use heap_4.c
Memory Handler definition
Memory allocation
void StartTask1(void const * argument)
{
/* USER CODE BEGIN 5 */
osPoolDef(Memory,0x100,uint8_t);
PoolHandle = osPoolCreate(osPool(Memory));
uint8_t* buffer=osPoolAlloc(PoolHandle);
/* Infinite loop */
for(;;)
{
osDelay(5000);
}
/* USER CODE END 5 */
}
/* Private variables ---------------------------------------------------------*/
osThreadId Task1Handle;
osPoolId PoolHandle;
Allocate memory from pool
Create memory pool

## Slide 48: FreeRTOS Tasks

## Slide 49: FreeRTOS Task states
Ready
  Tasks are ready to execute but are not currently executing because a different task with equal or higher priority is running
Running
  when task is actually running
Blocked
  Task is waiting for a either a temporal or external event
Suspended
  Task not available for scheduling
Suspend
Ready
Blocked
Runing
osThreadCreate
osThreadSuspend
osThreadSuspend
osThreadSuspend
osThreadResume
Blocked API function
Event
Scheduler

## Slide 50: FreeRTOS Task switch
Task switching on STM32?
Cortex cores have implemented few features which directly support os systems
Two interrupts dedicated for os
  PendSV interrupt
  SVC interrupt
Two stack pointers
  Process stack pointer
  Main stack pointer
SysTick timer
  Used to periodically trigger scheduling

## Slide 51: FreeRTOS OS interrupts
PendSV interrupt
  In this interrupt is the scheduler
  Lowest NVIC interrupt priority
  Not triggered by any periphery
  Pending state set from other interrupts
  Or from task which want end earlier (non MPU version)
SVC interrupt
  Interrupt risen by SVC instruction
  Called if task want end earlier (MPU version)
  In this interrupt set pending state PendSV (MPU version)
SysTick timer
  Set PendSV is context switch is necessary
Task1
Priority level
High priority
Low priority
time
Task2
PendSV
SysTick
SVC
Other IRQs
Task1
osDelay
Task2

## Slide 52: FreeRTOS Stack pointer
PendSV interrupt
Main stack pointer
  Used in interrupts
  Allocated by linker during compiling
Process stack pointer
  Each task have own stack pointer
  During context switch the stack pointer is initialized for correct task
Task 1
Task 2
Stack – Task 1
Data
Stack – Task 1
Data
Non scratch registers
Stack – Task 2
Data
Non scratch registers
Stack – Task 2
Data
PSP stack pointer
MSP stack pointer
PSP stack pointer

## Slide 53: Tasks API
Create task
Delete task
Get task ID
Task handle definition:
Create Task
osThreadId osThreadCreate (const osThreadDef_t *thread_def, void *argument)
osStatus osThreadTerminate (osThreadId thread_id)
osThreadId osThreadGetId (void)
/* Private variables ---------------------------------------------------------*/
osThreadId Task1Handle;
/* Create the thread(s) */
/* definition and creation of Task1 */
osThreadDef(Task1, StartTask1, osPriorityNormal, 0, 128);
Task1Handle = osThreadCreate(osThread(Task1), NULL);

## Slide 54: Tasks API
Check if task is suspended
Resume task
Check state of task
Suspend task
Resume all tasks
Suspend all tasks
osThreadState osThreadGetState(osThreadId thread_id)
osStatus osThreadIsSuspended(osThreadId thread_id)
osStatus osThreadSuspend (osThreadId thread_id)
osStatus osThreadResume (osThreadId thread_id)
osStatus osThreadSuspendAll (void)
osStatus osThreadResumeAll (void)

## Slide 55: Tasks lab
By default defined one defaultTask
Task is defined by
  Name
  Priority
  Stack size
  Name of entry function
Define two tasks
  Task1
  Task2
With same priority

## Slide 56: Tasks lab
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code

## Slide 57: Tasks lab
Any component in FreeRTOS need to have handle, very similar to CubeMX
Task function prototypes, names was taken from CubeMX
Before the scheduler is start we must create tasks
/* Private variables ---------------------------------------------------------*/
osThreadId Task1Handle;
osThreadId Task2Handle;
/* Private function prototypes -----------------------------------------------*/
void SystemClock_Config(void);
static void MX_GPIO_Init(void);
void StartTask1(void const * argument);
void StartTask2(void const * argument);
/* Create the thread(s) */
/* definition and creation of Task1 */
osThreadDef(Task1, StartTask1, osPriorityNormal, 0, 128);
Task1Handle = osThreadCreate(osThread(Task1), NULL);
/* definition and creation of Task2 */
osThreadDef(Task2, StartTask2, osPriorityNormal, 0, 128);
Task2Handle = osThreadCreate(osThread(Task2), NULL);
Define task parameters
Create task, allocate memory

## Slide 58: Tasks lab
Start the scheduler, the scheduler function newer ends
On first task run StartTask1 is called
Task must have inside infinity loop in case we don’t want to end the task
/* Start scheduler */
osKernelStart();
/* We should never get here as control is now taken by the scheduler */
void StartTask1(void const * argument)
{
/* USER CODE BEGIN 5 */
/* Infinite loop */
for(;;)
{
printf("Task 1\n");
osDelay(1000);
}
/* USER CODE END 5 */
}
Endless loop
osDealy will start context switch

## Slide 59: Tasks lab
Second loop is same as previous
Compile and run project in debug and watch terminal window
/* StartTask2 function */
void StartTask2(void const * argument)
{
/* USER CODE BEGIN StartTask2 */
/* Infinite loop */
for(;;)
{
printf("Task 2\n");
osDelay(1000);
}
/* USER CODE END StartTask2 */
}

## Slide 60: Tasks lab
If both Delays (osDelay) are processed the FreeRTOS is in idle state
Task1
Priority level
High priority
Low priority
time
osDelay
osDelay
Task2
Task1
Task1
osDelay
osDelay
Task2
Delay ends
Idle
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2

## Slide 61: Tasks lab
Without Delays the threads will be in running state or in Ready state
Use HAL_Delay
Task1
Priority level
High priority
Low priority
time
SysTick
SysTick
Task2
Task1
Task1
SysTick
SysTick
Task2
SysTick
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2

## Slide 62: Tasks lab
Set one task Higher priority
Double click on task for change
Button OK

## Slide 63: Tasks lab
After we send text for 5x times, put task to block state
Because task have high priority it allow to run lower priority task
/* USER CODE END 4 */
void StartTask1(void const * argument)
{
/* USER CODE BEGIN 5 */
uint32_t i = 0;
/* Infinite loop */
for(;;)
{
for (i = 0; i < 5; i++){
printf("Task 1\n");
HAL_Delay(50);
}
osDelay(1000);
}
/* USER CODE END 5 */
}
Helps not spam terminal
Block task

## Slide 64: Tasks lab
If higher priority task is not running we can print text from this task
/* StartTask2 function */
void StartTask2(void const * argument)
{
/* USER CODE BEGIN StartTask2 */
/* Infinite loop */
for(;;)
{
printf("Task 2\n");
HAL_Delay(50);
}
/* USER CODE END StartTask2 */
}
Helps not spam terminal

## Slide 65: Tasks lab
What happen when Task1 call osDelay?
Task1
Priority level
High priority
Low priority
time
osDelay
Delay end
Task2
Task1
Task1
Delay end
osDelay
Task2
osDelay
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2

## Slide 66: Tasks lab
What happen if Task1 does not call osDelay? Replace osDelay for HAL_Delay
Task1
Priority level
High priority
Low priority
time
HAL_Delay
HAL_Delay end
Task2
Task1
Task1
HAL_Delay end
HAL_Delay
Task2
HAL_Delay
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Suspend
Ready
Blocked
Runing
Task1
Task2
Task1
Task1
Task2
Task2

## Slide 67: osDelay API
Delay function
Delay function which measure time from which is delay measured
osStatus osDelay (uint32_t millisec)
osStatus osDelayUntil (uint32_t PreviousWakeTime, uint32_t millisec)

## Slide 68: osDelay function
Task 2
Pri 2
PendSV
Task 2
Pri 2
Task 1 - Pri 1
Task 2 - Pri 2
vTaskDelay
PendSV(idle)
vTaskDelay
Task 2
Delay end
Task 1
Pri 1
Delay time
osDelay start measure time from osDelay call

## Slide 69: osDelayUntil
Task 2
Pri 2
PendSV
Task 2
Pri 2
Task 1 - Pri 1
Task 2 - Pri 2
vTaskDelayUntil
PendSV(idle)
vTaskDelay
Task 2
Delay end
Task 1
Pri 1
DelayUntil time
osDelayUntil measure time from point which we selected
This allow us to call task in regular intervals

## Slide 70: osDelay and osDelayUntil
Enable vTaskDelayUntil in Include parameters
Regenerate project, modify tasks to:
void StartTask1(void const * argument)
{
/* USER CODE BEGIN 5 */
uint32_t i = 0;
/* Infinite loop */
for(;;)
{
printf("Task 1\n");
HAL_Delay(1000);
osDelay(2000);
}
/* USER CODE END 5 */
}
/* StartTask2 function */
void StartTask2(void const * argument)
{
/* USER CODE BEGIN StartTask2 */
/* Infinite loop */
for(;;)
{
printf("Task 2\n");
HAL_Delay(200);
}
/* USER CODE END StartTask2 */
}
Delay between two run is 2s

## Slide 71: osDelay and osDelayUntil
Enable vTaskDelayUntil in Include parameters
Regenerate project, modify tasks to:
void StartTask1(void const * argument)
{
/* USER CODE BEGIN 5 */
uint32_t wakeuptime;
/* Infinite loop */
for(;;)
{
wakeuptime=osKernelSysTick();
printf("Task 1\n");
HAL_Delay(1000);
osDelayUntil(wakeuptime,2000);
}
/* USER CODE END 5 */
}
Function will be executed every 2s
Real delay time
Time from which is delay measured
For osDelayUntil function we need mark wakeup time

## Slide 72: Priority change lab
Task1 have higher priority than Task2
If not enable vTaskPriorityGet and uxTaskPrioritySet in IncludeParameters

## Slide 73: Priority change lab
Modify Task1 to:
void StartTask1(void const * argument)
{
/* USER CODE BEGIN 5 */
osPriority priority;
/* Infinite loop */
for(;;)
{
priority=osThreadGetPriority(Task2Handle);
printf("Task 1\n");
osThreadSetPriority(Task2Handle,priority+1);
HAL_Delay(1000);
}
/* USER CODE END 5 */
}
Increase Task2 priority
Reads Task2 priority

## Slide 74: Priority change lab
Modify Task2 to:
/* StartTask2 function */
void StartTask2(void const * argument)
{
/* USER CODE BEGIN StartTask2 */
osPriority priority;
/* Infinite loop */
for(;;)
{
priority=osThreadGetPriority(NULL);
printf("Task 2\n");
osThreadSetPriority(NULL,priority-2);
}
/* USER CODE END StartTask2 */
}
Decrease task priority
Read priority of current task

## Slide 75: Priority change lab
How priorities are changed?
Task 1
Pri 6
PendSV
Task 1
Pri 6
Task 1 - Pri 6
Task 2 - Pri 4
vTaskPrioritySet
Task 2 Pri +1
Task 2
Pri 6
PendSV
vTaskPrioritySet
Task 2 Pri -2
vTaskPrioritySet
Task 2 Pri +1
PendSV
Task 1
Pri 6
Task 2 - Pri 5
Task 2 - Pri 6
Task 2 - Pri 4

## Slide 76: Creating and deleting tasks lab
Example how to create and delete tasks
Comment Task2 creation part in main.c
Modify Task1 to create task2
/* definition and creation of Task2 */
// osThreadDef(Task2, StartTask2, osPriorityNormal, 0, 128);
// Task2Handle = osThreadCreate(osThread(Task2), NULL);
void StartTask1(void const * argument)
{
/* USER CODE BEGIN 5 */
/* Infinite loop */
for(;;)
{
printf("Create task2\n");
osThreadDef(Task2, StartTask2, osPriorityNormal, 0, 128);
Task2Handle = osThreadCreate(osThread(Task2), NULL);
osDelay(1000);
}
/* USER CODE END 5 */
}
Task 2 creation

## Slide 77: Creating and deleting tasks lab
Example how to create and delete tasks
Modift Task2 to delete him-self:
/* StartTask2 function */
void StartTask2(void const * argument)
{
/* USER CODE BEGIN StartTask2 */
/* Infinite loop */
for(;;)
{
printf("Delete Task2\n");
osThreadTerminate(Task2Handle);
}
/* USER CODE END StartTask2 */
}
Delete Task

## Slide 78: Creating and deleting tasks lab
Example how to create and delete tasks
Task 1
Pri 1
Task 1
Pri 1
Task 1 - Pri 1
vTaskDelay
PendSV(idle)
Task 1
Delay end
Task 2
Pri 2
vTaskDelete
xTaskCreate
Task 1
Pri 1
PendSV
PendSV

## Slide 79: FreeRTOS Queues

## Slide 80: Queue
Receiver Task
osMessageGet
Receiver Task
Receiver Task
Receiver Task
osMessageGet
Receiver Task
Message 2
Message 2
Message 1
Message 1
Sender Task
osMessagePut
Message 1
Sender Task
osMessagePut
Sender Task
Sender Task
Sender Task
Message 2

## Slide 81: Queue
Create Queue:
Put data into Queue
Receive data from Queue
osMessageQId osMessageCreate (const osMessageQDef_t *queue_def, osThreadId thread_id)
osStatus osMessagePut (osMessageQId queue_id, uint32_t info, uint32_t millisec)
osEvent osMessageGet (osMessageQId queue_id, uint32_t millisec)
Create Queue
Queue Handle
Item to send
Queue Handle
Send timeout
Queue handle
Structure with status and with received item
Receiving timeout

## Slide 82: Queue
osEvent structure
If we want to get data from osEvent we must use:
  osEventName.v if the value is 32bit message(or 8/16bit)
  osEventName.p and retype on selected datatype
typedef struct {
osStatus status; ///< status code: event or error information
union {
uint32_t v; ///< message as 32-bit value
void *p; ///< message or mail as void pointer
int32_t signals; ///< signal flags
} value; ///< event value
union {
osMailQId mail_id; ///< mail id obtained by \ref osMailCreate
osMessageQId message_id; ///< message id obtained by \ref osMessageCreate
} def; ///< event definition
} osEvent;

## Slide 83: Queue lab
Set both tasks to normal priority
Queue part
Button Add
Set queue size to 256
Queue type to uint8_t
Button OK

## Slide 84: Queue lab
Queue handler is now defined
Queue item type initialization, length definition and create of queue and memory allocation
/* Private variables ---------------------------------------------------------*/
osThreadId Sender1Handle;
osThreadId ReceiverHandle;
osMessageQId Queue1Handle;
/* Create the queue(s) */
/* definition and creation of Queue1 */
osMessageQDef(Queue1, 256, uint8_t);
Queue1Handle = osMessageCreate(osMessageQ(Queue1), NULL);
Queue item definition
Queue size

## Slide 85: Queue lab
Sender1 task
void StartSender1(void const * argument)
{
/* USER CODE BEGIN 5 */
/* Infinite loop */
for(;;)
{
printf("Task1\n");
osMessagePut(Queue1Handle,0x1,200);
printf("Task1 delay\n");
osDelay(1000);
}
/* USER CODE END 5 */
}
Put value ‘1’ into queue
Queue handle
Item to send
Timeout for send

## Slide 86: Queue lab
Receiver task
/* StartReceiver function */
void StartReceiver(void const * argument)
{
/* USER CODE BEGIN StartReceiver */
osEvent retvalue;
/* Infinite loop */
for(;;)
{
printf("Task2\n");
retvalue=osMessageGet(Queue1Handle,4000);
printf("%d \n",retvalue.value.p);
}
/* USER CODE END StartReceiver */
}
Get item from queue
Queue handle
How long we wait on data in queue
It will Block task

## Slide 87: Queue Blocking
Receiver Task
Blocked
Receiver Task
Receiver Task
Blocked
Receiver Task
Blocked
Sender Task
Receiver Task
osMessageGet
Receiver Task
Message 1
Sender Task
Message 1
osMessagePut
Sender Task
Sender Task
osMessageGet
osMessageGet

## Slide 88: Queue Blocking
Receiver Pri 1
PendSV
Sender1 Pri 1
Sender1- Pri 1
xQueueReceive
Sender1 Pri 1
Receiver- Pri 1
PendSV
xQueueSend
Receiver Pri 1
PendSV
xQueueReceive
After calling osMessageGet
If any data are not in queue the task is blocked for settable time
If the data is in queue the task will continue

## Slide 89: Two senders lab
Two sending tasks
One receivers tasks
Same priorities

## Slide 90: Two senders lab
Two sending tasks
They are same no change necessary
void StartSender1(void const * argument)
{
/* USER CODE BEGIN 5 */
/* Infinite loop */
for(;;)
{
printf("Task1\n");
osMessagePut(Queue1Handle,0x1,200);
printf("Task1 delay\n");
osDelay(2000);
}
/* USER CODE END 5 */
}
void StartSender2(void const * argument)
{
/* USER CODE BEGIN StartSender2 */
/* Infinite loop */
for(;;)
{
printf("Task2\n");
osMessagePut(Queue1Handle,0x2,200);
printf("Task2 delay\n");
osDelay(2000);
}
/* USER CODE END StartSender2 */
}

## Slide 91: Two senders lab
Simple receiver
/* StartReceiver function */
void StartReceiver(void const * argument)
{
/* USER CODE BEGIN StartReceiver */
osEvent retvalue;
/* Infinite loop */
for(;;)
{
retvalue=osMessageGet(Queue1Handle,4000);
printf("Receiver\n");
printf("%d \n",retvalue.value.p);
}
/* USER CODE END StartReceiver */
}

## Slide 92: Two senders lab
What we can see in debug now?
Because tasks have same priority, receiver will get data from queue after both task put data into queue
What would happen if there were more tasks?
Receiver Pri 1
PendSV
Sender1- Pri 1
xQueueReceive
Sender1 Pri 1
Receiver- Pri 1
xQueueSend
Sender2- Pri 1
Sender1 Pri 1
PendSV
Receiver Pri 1
PendSV
xQueueReceive
PendSV
Sender2 Pri 1
xQueueSend

## Slide 93: Receiver with higher priority lab
Senders have same priority
Receiver have higher priority than senders

## Slide 94: Receiver with higher priority lab
Receiver is now unblocked every time when sender tasks put data into queue
Receiver Pri 2
PendSV
Sender2 Pri 1
Sender1- Pri 1
Sender2- Pri 1
xQueueReceive
Sender1 Pri 1
Receiver- Pri 2
PendSV
xQueueSend
Receiver Pri 2
PendSV
xQueueReceive
Sender1 Pri 1
PendSV
xQueueSend
Receiver Pri 2
xQueueReceive

## Slide 95: Queue items lab
Queues allow to define type (different variables or structures) which the queue use.
Regenerate project

## Slide 96: Queue items lab
Item size will be structure called Data

## Slide 97: Queue items lab
Create new structure type for data
Define Structures which will be sent from sender task
/* Define the structure type that will be passed on the queue. */
typedef struct
{
uint8_t Value;
uint8_t Source;
} Data;
/* Declare two variables of type Data that will be passed on the queue. */
Data DataToSend1={10,1};
Data DataToSend2={20,2};

## Slide 98: Queue items lab
Sent data from Sender1 task
void StartSender1(void const * argument)
{
/* USER CODE BEGIN 5 */
/* Infinite loop */
for(;;)
{
printf("Task1\n");
osMessagePut(Queue1Handle,(uint32_t)&DataToSend1,200);
printf("Task1 delay\n");
osDelay(2000);
}
/* USER CODE END 5 */
}
Put data into queue

## Slide 99: Queue items lab
Sent data from Sender2 task
void StartSender2(void const * argument)
{
/* USER CODE BEGIN 5 */
/* Infinite loop */
for(;;)
{
printf("Task2\n");
osMessagePut(Queue1Handle,(uint32_t)&DataToSend2,200);
printf("Task2 delay\n");
osDelay(2000);
}
/* USER CODE END 5 */
}
Put data into queue

## Slide 100: Queue items lab
/* StartReceiver function */
void StartReceiver(void const * argument)
{
/* USER CODE BEGIN StartReceiver */
osEvent retvalue;
/* Infinite loop */
for(;;)
{
retvalue=osMessageGet(Queue1Handle,4000);
if(((Data*)retvalue.value.p)->Source==1){
printf("Receiver Receive message from Sender 1\n");
}else{
printf("Receiver Receive message from Sender 2\n");
}
printf("Data: %d \n",((Data*)retvalue.value.p)->Value);
}
/* USER CODE END StartReceiver */
}
Receiver data from sender task
Get data from queue
Decode data from osEvent structure

## Slide 101: FreeRTOS Semaphores

## Slide 102: Semaphores
Used for synchronization between
  Tasks
  Interrupt and task
Two types
  Binary semaphores
  Counting semaphores
Binary semaphore
  Have only one ‘token’
  Using to synchronize one action
Counting semaphore
  Have multiple ‘tokens’
  Synchronize multiple actions

## Slide 103: Binary Semaphore
Task2
Blocked
Task2
Task2
Task2
Blocked
Task1
osSemaphoreWait
Task2
Blocked
Task1
osSemaphoreRelease
osSemaphoreWait
Task1
osSemaphoreWait
Task2
Task1
osSemaphoreRelease
Task2
Task1
osSemaphoreWait

## Slide 104: Binary Semaphore
Semaphore creation
Wait for Semaphore release
Semaphore release
osSemaphoreId osSemaphoreCreate (const osSemaphoreDef_t *semaphore_def, int32_t count)
int32_t osSemaphoreWait (osSemaphoreId semaphore_id, uint32_t millisec)
osStatus osSemaphoreRelease (osSemaphoreId semaphore_id)
Semaphore handle
Semaphore definition
Semaphore ‘tokens’ For binary semaphore is 1
Semaphore handle
How long wait for semaphore release
Semaphore handle
Return status
Number of ‘tokens in semaphore’

## Slide 105: Binary Semaphore lab
Create two tasks
With same priority
Button Add
Set parameters
Button OK

## Slide 106: Binary Semaphore lab
Create binary binary semaphore
Button Add
Set name
Button OK

## Slide 107: Binary Semaphore lab
Semaphore handle definition
Semaphore creation
/* Private variables ---------------------------------------------------------*/
osThreadId Task1Handle;
osThreadId Task2Handle;
osSemaphoreId myBinarySem01Handle;
/* Create the semaphores(s) */
/* definition and creation of myBinarySem01 */
osSemaphoreDef(myBinarySem01);
myBinarySem01Handle = osSemaphoreCreate(osSemaphore(myBinarySem01), 1);

## Slide 108: Binary Semaphore lab
Semaphore use
If tasks/interrupt is done the semaphore is released
void StartTask1(void const * argument)
{
/* USER CODE BEGIN 5 */
/* Infinite loop */
for(;;)
{
osDelay(2000);
printf("Task1 Release semaphore\n");
osSemaphoreRelease(myBinarySem01Handle);
}
/* USER CODE END 5 */
}

## Slide 109: Binary Semaphore lab
Semaphore Wait
Second task waits on semaphore release After releasetask is unbocked and continue in work
void StartTask2(void const * argument)
{
/* USER CODE BEGIN StartTask2 */
/* Infinite loop */
for(;;)
{
osSemaphoreWait(myBinarySem01Handle,4000);
printf("Task2 synchronized\n");
}
/* USER CODE END StartTask2 */
}

## Slide 110: Binary Semaphore lab
Task1 is synchronized with Task2
Task1 - Pri 1
Task2 - Pri 1
Task1 Pri 1
PendSV
osSemaphore Wait
Task2 Pri 1
PendSV
osSemaphore Release
Task1 Pri 1
PendSV
osSemaphore Wait
Task2 Pri 1

## Slide 111: Counting semaphore
Os API same as Binary semaphore
Semaphore creation
Wait for Semaphore release
Semaphore release
osSemaphoreId osSemaphoreCreate (const osSemaphoreDef_t *semaphore_def, int32_t count)
int32_t osSemaphoreWait (osSemaphoreId semaphore_id, uint32_t millisec)
osStatus osSemaphoreRelease (osSemaphoreId semaphore_id)

## Slide 112: Counting Semaphore
Task3
Blocked
Task3
Task3
Task3
Task3
Task2
Task2
Task1
osSemaphoreRelease
Task1
osSemaphoreRelease
Task2
Blocked
Task3
Task2
osSemaphoreWait
Task1
Task2
Blocked
Task3
Task2
osSemaphoreWait
Task1
Task2
osSemaphoreWait
Task1

## Slide 113: Counting Semaphore lab
Create three tasks
With same priority
Button Add
Set parameters
Button OK

## Slide 114: Counting Semaphore lab
Create Counting semaphore
Set count of tokens
Button Add
Set name
Button OK

## Slide 115: Counting Semaphore lab
Create Counting semaphore
Task1 and Task2 will be same
/* Create the semaphores(s) */
/* definition and creation of myCountingSem01 */
osSemaphoreDef(myCountingSem01);
myCountingSem01Handle = osSemaphoreCreate(osSemaphore(myCountingSem01), 2);
void StartTask1(void const * argument)
{
/* USER CODE BEGIN 5 */
/* Infinite loop */
for(;;)
{
osDelay(2000);
printf("Task1 Release counting semaphore\n");
osSemaphoreRelease(myCountingSem01Handle);
}
/* USER CODE END 5 */
}
void StartTask2(void const * argument)
{
/* USER CODE BEGIN StartTask2 */
/* Infinite loop */
for(;;)
{
osDelay(2000);
printf("Task2 Release counting semaphore\n");
osSemaphoreRelease(myCountingSem01Handle);
}
/* USER CODE END StartTask2 */
}

## Slide 116: Counting Semaphore lab
Task3 will wait until semaphore will be 2 times released
void StartTask3(void const * argument)
{
/* USER CODE BEGIN StartTask3 */
/* Infinite loop */
for(;;)
{
osSemaphoreWait(myCountingSem01Handle, 4000);
osSemaphoreWait(myCountingSem01Handle, 4000);
printf("Task3 synchronized\n");
}
/* USER CODE END StartTask3 */
}

## Slide 117: Counting Semaphore lab
Task1 and Task2 release semaphore
Task 3 wait for two tokens
Task1- Pri 1
Task2- Pri 1
Task3
Pri 1
PendSV
osSemaphore Wait
Task1
Pri 1
PendSV
osSemaphore Release
Task2 Pri 1
PendSV
osSemaphore Release
Task3 Pri 1
Task3- Pri 1
Task3
Pri 1
PendSV
osSemaphore Wait
Task1
Pri 1
osSemaphore Release
osSemaphore Wait

## Slide 118: FreeRTOS Mutex

## Slide 119: Mutex
Task2 Blocked
Task2
Task2
Blocked
Resourse
Resource
Task1
osMutexWait
Task2 Blocked
Resourse
Task1
osMutexRelease
Resource
Resourse
Task2
Resource
Task1
osMutexWait
Task2
Resourse
Task1
osMutexRelease
Resource
osMutexWait
osMutexWait
Used to guard access to limited resource
Work very similar as Semaphores

## Slide 120: Mutex
Mutex creation
Wait for Mutex release
Mutex release
osMutexId osMutexCreate (const osMutexDef_t *mutex_def)
osStatus osMutexWait (osMutexId mutex_id, uint32_t millisec)
osStatus osMutexRelease (osMutexId mutex_id)
Mutex handle
Mutex definition
Mutex handle
How long wait for mutex release
Mutex handle
Return status
Return status

## Slide 121: Mutex lab
Create two tasks
With same priority
Button Add
Set parameters
Button OK

## Slide 122: Mutex lab
Create Mutex
Button Add
Set name
Button OK

## Slide 123: Mutex lab
Both tasks using printf function.
Mutex is used to avoid collisions
Task1- Pri 1
Task1
Pri 1
Task2- Pri 1
PendSV
osMutexWait
Task2
Pri 1
osMutexRelease
Print
osDelay
osMutexWait
Print
Only one task can have semaphore

## Slide 124: Mutex lab
Mutex handle definition
Mutex creation
/* Private variables ---------------------------------------------------------*/
osThreadId Task1Handle;
osThreadId Task2Handle;
osMutexId myMutex01Handle;
/* Create the mutex(es) */
/* definition and creation of myMutex01 */
osMutexDef(myMutex01);
myMutex01Handle = osMutexCreate(osMutex(myMutex01));

## Slide 125: Mutex lab
Task1 and Task2 using of Mutex
void StartTask1(void const * argument)
{
/* USER CODE BEGIN 5 */
/* Infinite loop */
for(;;)
{
osDelay(2000);
osMutexWait(myMutex01Handle,1000);
printf("Task1 Print\n");
osMutexRelease(myMutex01Handle);
}
/* USER CODE END 5 */
}
void StartTask2(void const * argument)
{
/* USER CODE BEGIN StartTask2 */
/* Infinite loop */
for(;;)
{
osDelay(2000);
osMutexWait(myMutex01Handle,1000);
printf("Task2 Print\n");
osMutexRelease(myMutex01Handle);
}
/* USER CODE END StartTask2 */
}

## Slide 126: FreeRTOS Software Timers

## Slide 127: Software Timers
Software timer is one of component in RTOS
Can extend number of Timers in STM32
Are not precise but can handle periodic actions or delay actions
Two modes
  Periodic
  One Pulse
Task1
osTimerStart
Software timer counting
Software Timer Callback
Software timer counting
Software Timer Callback
Software timer counting
Task1
osTimerStart
Software timer counting
Software Timer Callback

## Slide 128: Software Timers
Software timer creation
Software timer start
Software timer stop
osTimerId osTimerCreate (const osTimerDef_t *timer_def, os_timer_type type, void *argument)
osStatus osTimerStart (osTimerId timer_id, uint32_t millisec)
osStatus osTimerStop (osTimerId timer_id)
Timer handle
Timer definition
Timer handle
Timer period
Timer handle
Return status
Return status
Repeat timing or onetime timing

## Slide 129: Software Timers lab
Software timers are by default disabled in CubeMX
FreeRTOS configuration
Configuration TAB
Enable Software timers

## Slide 130: Software Timers lab
Create one task
Button Add
Set parameters
Set name
Button OK

## Slide 131: Software Timers lab
Create Timer
Button Add
Set timer name
Timer callback name
Button OK

## Slide 132: Software Timers lab
Software timer handle definition
Software timer creation
Software timer start
/* Private variables ---------------------------------------------------------*/
osThreadId Task1Handle;
osTimerId myTimer01Handle;
/* Create the timer(s) */
/* definition and creation of myTimer01 */
osTimerDef(myTimer01, Callback01);
myTimer01Handle = osTimerCreate(osTimer(myTimer01), osTimerPeriodic, NULL);
void StartTask1(void const * argument)
{
/* USER CODE BEGIN 5 */
osTimerStart(myTimer01Handle,1000);
/* Infinite loop */
for(;;)
{
osDelay(2000);
printf("Task1 Print\n");
}
/* USER CODE END 5 */
}

## Slide 133: Software Timers lab
Software timer callback
/* Callback01 function */
void Callback01(void const * argument)
{
/* USER CODE BEGIN Callback01 */
printf("Timer Print\n");
/* USER CODE END Callback01 */
}

## Slide 134: Questions???
There are other features, as the advanced HOOK
  In the web, there is an example of this feature applied
    www.github.com/montanari9

## Slide 135: End Thanks for your attention